## Slide 1
42-Pin Receptacle
19-Pin
A Receptacle
19-Pin
B Receptacle
19-Pin
C Receptacle
Signal
Conditioning
Board
R TR-A
R TR-B
R TR-C
R CL-A
R CL-B
R CL-C
Relay
FI-A
Relay
FI-B
Relay
FI-C
CN1 – Molex 12pins
From 42-pin
CN2 – 3pins Large
CN3 – Molex 12pins
To 19-pin
12V to 24V Converter
42-Pin Junction Box Harness
Vishay AC07000001502JAC00,
15kΩ, 5%, 7W
Part#

## Slide 2
42-Pin Connector | SS Junction Box Pins
1 | 19A-L
2 | CN1-2
3 | CN1-1
4 | CN1-4
5 | CN1-3
6 | CN1-6
7 | CN1-5
8 | 19B-L
9 | 19C-L
10 | CN1-10
11 | CN1-11
12 | CN1-7
13 | CN1-8
14 | CN1-9
15 | 19A-P, 19B-P, 19C-P
16 | 19C-M
17 | 19B-M
18 | 
19 | 
20 | 
21 | 19A-A
22 | 19A-M
23 | 
24 | 
25 | CN1-11
26 | 
27 | 19A-C, 19B-C, 19C-C
28 | 19B-A
29 | 
30 | 19A-N
31 | 19B-N
32 | 19C-N
33 | 19A-N
34 | 19B-N
35 | 19C-A
36 | 19A-F
37 | 19B-F
38 | 19C-F
39 | 19C-N
40 | 19A-E
41 | 19B-E
42 | 19C-E
CN3 Pin | SS Junction Box Pins
1 | 19A-H
2 | 19A-G
3 | 19B-H
4 | 19B-G
5 | 19C-H
6 | 19C-G
7 | 19A-R
8 | 19B-R
9 | 19C-R
10 | 19A-J, 19B-J, 19C-J
11 | 19A-K, 19B-K, 19C-K
12 | 
42-Pin Junction Box Harness Pin Map

## Slide 3
Pin | Signal
1 | Trip 1 (155V)
2 | Close 1 (155V)
3 | Trip 2 (155V)
4 | Close 2 (155V)
5 | Trip 3 (155V)
6 | Close 3 (155V)
7 | Fault Ind A (12V)
8 | Fault Ind B (12V)
9 | Fault Ind C (12V)
10 | 12V DC Power
11 | Gnd
12 | 
CN1
Pin | Signal
1 | Trip A (24V)
2 | Close A (24V)
3 | Trip B (24V)
4 | Close B (24V)
5 | Trip C (24V)
6 | Close C (24V)
7 | Fault Ind A (24V)
8 | Fault Ind B (24V)
9 | Fault Ind C (24V)
10 | 24V DC Power
11 | Gnd
12 | 
CN3
Pin | Signal
1 | 12V DC Power
2 | Gnd
3 | 24V DC Power
CN2
Signal Conditioning Board Pin Outs
CN2-3 to CN3-10
Make a very wide trace to handle 5A continuous